## Slide 1: Description of OA Technology
Date: March, 2016
By: Dual Aperture International
Center for Integrated Smart Sensors

## Slide 2: 0. OAIP Overview

## Slide 3: Direct Depth technology based on Offset IR Aperture
Direct advantages over
  DFD
  Stereo camera
  Earlier OA
  Software-centric approach

## Slide 4: Why call ‘direct depth’? -Compared to DFD (blur-based)-
Edge extraction not needed, maybe optional for compute time reduction purpose.
  Direct disparity-based depth calculation using
    correlation and its credence for thresholding and
PSF and convolution are not needed; directly correlate in the raw image domain.
  Moving into the blurred domain using synthetic blurring lowers accuracy besides additional computing
Obtain absolute depth directly instead of PSF index which needs to be translated into absolute depth through calibration.
Ambiguity of depth around focal plane resolved.

## Slide 5: Why call ‘direct depth’? -Compared to stereo camera-
Neither calibration nor alignment needed.
Size(two cameras + baseline), cost reduced

## Slide 6: Why call ‘direct depth’? -Compared to earlier offset aperture-
In RGB offset aperture camera where R, G, and B apertures are offset from each other, RGB image restoration is too difficult.
The proposed Offset IR aperture camera uses mutually horizontally offset apertures between RGB and IR.
RGB image quality is not deteriorated except the RGB aperture can be somewhat offset from the center. [White/SIR filter desirable]

## Slide 7: Why call ‘direct depth’? -Compared to earlier software(-based) approach-
Hardware design based on smart memory architecture is easier; start from basic features and gradually upgrade, i.e., scalable architecture is possible to advance with the market requirement
Extremely fast depth computing hardware design is possible using scanline processing unit design; real-time or direct (fast) availability of depth

## Slide 8: Introduction
Principle of Offset Aperture (OA) depth extraction
  The offset-aperture creates a disparity which varies with the object distance.
  Thus, Object distance can be estimated by measuring the disparity between RGB and IR image.
Sensor
Near object
Far object
RGB
aperture
IR
aperture
RGB image
IR image
Far object disparity
RGB image
IR image
Near object disparity
(Top view)
Fig. 0.1. Principle of OA

## Slide 9: Introduction
Composition of the camera
RGB cut-off filter
RGB pass
IR pass
4 color CIS
G | R
B | IR
Fig. 0.2. Structure of the camera where (a) shows the lateral view of OA camera, (b) shows the aperture and (c) shows the four-color sensor used in the camera.
(a)
(b)
(c)

## Slide 10: Introduction
Spectral characteristic
Chart: Wavelength (nm)
R G B IR
R G B
IR
RGB cut-off filter (IR pass)
IR cut-off filter (RGB pass)
(2nd round aperture)
Fig. 0.3. (a) Vertical cross section of the aperture and (b) the corresponding spectral response curve.
(a)
(b)

## Slide 11: Introduction
Depth extraction algorithm for OA camera
  Object distance is estimated by measuring the disparity between RGB patch and IR patch.
RGB patch
IR patch
Similarity measure
Similarity measure
Similarity measure
Similarity measure
…
Similarity
score
n
Disparity
(Depth)
IR patch
IR patch
IR patch
…
RGB image
RGB patch
IR image
IR patches
…
Fig. 0.4. Graphical illustration of depth extraction using OA camera, where (a) shows the RGB and IR images with the respective patches and (b) shows the correlation curve.
(a)
(b)

## Slide 12
ED
CA
NR
LC
IDE-E
FDE-E
FDE-A
GE
IDE-A
RGB/IR image
Sparse depthmap
Full depthmap
LC : Leakage compensation
NR : Noise reduction
ED : Edge detection
GE : Gradient extraction
IDE-E : Integer disparity estimation for edge pixels
IDE-A : Integer disparity estimation for all pixels
CA : Cost aggregation
FDE-E : Fractional disparity estimation for edge pixels
FDE-A : Fractional disparity estimation for all pixels
DME
(Depth Map Engine)
Fig. 0.5. Block diagram with the data-flow of the depth extraction system based on OA camera.
Introduction

## Slide 13: Introduction
Functional blocks of OAIP
  Pre-processing
    Leakage compensation(LC)
    Noise reduction(NR)
    Edge detection(ED)
  Core processing
    Gradient extraction(GE)
    Integer disparity estimation(IDE)
  Post-processing
    Cost aggregation(CA)
    Fractional disparity estimation(FDE)

## Slide 14: Pre-Processing
Leakage compensation(LC)
  Since the RGB and IR response curves overlap, crosstalk occurs between the RGB and IR images.
  We compensate for the cross-spectral crosstalk by subtracting scaled signals.
  Correction is performed using the following equations.
R G B IR
R G B
IR
IR pass filter
RGB pass filter
Fig. 0.6. (a)Structure of aperture and leakage from (b) RGB to IR and from (c) IR to RGB.
(b)
(c)
(a)

## Slide 15: Pre-Processing
Leakage compensation(LC)
  We can calculate leakage ratio of light sources by spectrum analysis.
  Refinement model
Block IR rays using IR cut filter
Capture the white image

  ,
Block RGB rays using RGB cut filter
Capture the out-focus images of white target in various light conditions

,
Fig. 0.7. White checker

## Slide 16: Pre-Processing
Noise reduction(NR)
  The objective of this block is to
    Enhance SNR(Signal to Noise Ratio)
    Preserve edges and textures in the image
  Our experiments show that Bilateral Filter shown the best performance based on quantitative and qualitative depthmap evaluation
Fig. 0.8. (a) Reference image, (b) depthmap extracted from the noisy image, (c) depthmap extracted from temporally averaged image (benchmark) and (d) depthmap extracted after applying bilateral filter to input images.
(b)
(c)
(d)
(a)

## Slide 17: Results
Leakage Comp
Image NR
NCC based Stereo Matching
(35x35)
Cost Agg
Guided Filter
35x35
(e)
(b)
(c)
(f)
(d)
Method | Error% | MSE
Box | 42% | 10.6
HSP | 41.9% | 10.5
BF | 36% | 8.1
Guided | 46.3% | 10.3
Pre-Processing
Fig. 0.9. (a) Input scene, (b) benchmark, (c) box, (d) HSP, (e) BF, and (f) guided
(a)

## Slide 18: Core Processing
Gradient extraction(GE)
  Gradient exaggerates the changes in an image, resultantly, the selectivity of similarity curve with disparity is improved.
Integer disparity estimation(IDE)
  NCC and ZNCC have shown the best performance based on qualitative evaluation.

## Slide 19: Post-Processing
Cost aggregation(CA)
  Cost aggregation methods are used to refine the depth map.
  These consider the disparity of neighboring pixels and make a decision about the actual disparity of current pixel.
  Semi-Global Matching (SGM) aggregates cost over the complete path to a pixel.
  For example, the aggregated cost of pixels for a path from left to right is given by
  Key advantage of SGM is that it is a greedy algorithm.
    Aggregated cost is computed by using only the aggregated cost of previous pixel.
  First term maintains a smooth depth.
  Second and third term allow depth to change smoothly but with a small penalty .
  Last term applies a large penalty to sudden change in depth where is inversely related to intensity gradient.
  Thus, SGM includes both color similarity and depth congruence.

## Slide 20: Post-Processing
  Number of paths
    In the papers, authors use 16 paths to the pixel.
    Using 8 paths also provide decent results.
    However, for hardware implementation, using only 4 paths is feasible.
    For this, we have to maintain the aggregated costs of all pixels above and one to the left of the given pixel.
(a)
(b)
(c)
(d)
(e)
Fig. 0.10. (a) The number of paths proposed in the original paper, (b) the number of paths that can be used for hardware implementation, (c) Reference image, (d) SGM result with high image PSNR and (c) SGM result with low image PSNR

## Slide 21: Post-Processing
Fractional disparity estimation(FDE)
  Fractional disparity extraction can be utilized to increase the depth resolution.
  By applying curve-fitting to a second-order polynomial, we extract fractional disparity.
Chart: Disparity
| -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Correlation | 0.68 | 0.79 | 0.85 | 0.88 | 0.87 | 0.81 | 0.71 | 0.6
Estimated disparity before FDE is 0.
Estimated disparity after FDE is is 0.1666.
Example:

## Slide 22: Experimental Environments
Camera
  CIS model : Hi231 - 4 color (RGB IR)
  CIS resolution : 1956x1232 (2.4M) 10bits
  Lens type : M12 (CCTV lens)
  Focal length : 8mm
Test aperture (unit : mm)
Test light source
  Fluorescent
RGB
IR
5
3.5
1.5
1.5

## Slide 23: Results
Disparity resolution
6cm
106cm
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Patch size : 75x35
Search range : -30 ~ 7 pixels
Light source : Fluorescent
…
<Test scene>
6cm ~ 106cm
(interval : 1cm, 101 levels)
(a)
(b)
Fig. 0.11. (a) Test scene and (b) disparity-distance relationship.

## Slide 24: Results
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent
Fig. 0.12. Input scene

## Slide 25: Results
Far
Near
(a)
(b)
(c)
Fig. 0.13. (a) Input scene, (b) sparse depthmap and (c) full depthmap.
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent

## Slide 26: Results
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent
Fig. 0.14. Input scene

## Slide 27: Results
Far
Near
(a)
(b)
(c)
Fig. 0.15. (a) Input scene, (b) sparse depthmap and (c) full depthmap.
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent

## Slide 28: Results
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent
Fig. 0.16. Input scene

## Slide 29: Results
(a)
Far
Near
(b)
(c)
Fig. 0.17. (a) Input scene, (b) sparse depthmap and (c) full depthmap.
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent

## Slide 30: Results
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent
Fig. 0.18. Input scene

## Slide 31: Results
Far
Near
(a)
(b)
(c)
Fig. 0.19. (a) Input scene, (b) sparse depthmap and (c) full depthmap.
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent

## Slide 32: Results
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent
Fig. 0.20. Input scene

## Slide 33: Results
Far
Near
(a)
(b)
(c)
Fig. 0.21. (a) Input scene, (b) sparse depthmap and (c) full depthmap.
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 40cm
Kernel size : 33x33
Search range : -20 ~ 5 pixels
Light source : Fluorescent

## Slide 34: Execution Time
Chart: 
| Sparse Depth Map | Full Depth Map
Leakage compensation(LC) | 0.005 | 0.005
Edge detection(ED) | 0.08 | 0
Noise reduction(NR) | 0.816 | 0.816
Gradient extraction(GE) | 0.016 | 0.016
Integer disparity estimation(IDE) | 0.468 | 0.468
Cost aggregation(CA) | 0 | 0.8
Fractional disparity estimation(FDE) | 0.016 | 0.218
Total exe. time : 1.401 s
Total exe. time : 2.323s
(unit : seconds)
Fig. 0.22. Computation time of OAIP

## Slide 35: 1. Leakage Compensation(LC)

## Slide 36: Pre-Processing
Leakage compensation
  Since the RGB and IR response curves overlap, crosstalk occurs between the RGB and IR images.
  We compensate for the cross-spectral crosstalk by subtracting scaled signals.
  Correction is performed using the following equations.
Fig. 1.1. Leakage from (a) RGB to IR and from (b) IR to RGB.
(a)
(b)

## Slide 37: Functional Overview
Calculating leakage ratio by spectral analysis
  We observe spectrum distribution with different light sources, aperture filters and sensor filters.
  To exclude the effect of surface reflectance, we use a white checker in the experiments.
Refinement model
  We perform weighted subtraction of one image from another.
  The weight is directly proportional to the leakage ratio which is defined in coming slides.
  We compute 4 parameters
    R to IR ratio
    IR to Red ratio
    IR to Green ratio
    IR to Blue ratio

## Slide 38: Functional Description
Refinement model
  Spectral analysis was performed to compute leakage ratio.
Cut the IR rays
Capture the white image

Cut the RGB rays
Capture the out-focus images of white target in various light conditions

(b)
(a)
Fig. 1.2. (a) The white checker used in the experiments and (b) the ideal spectral response.

## Slide 39: Functional Results
Far
Near
(a)
(b)
(c)
(d)
(e)
(f)
Fig. 1.3. Results at CWF light source (a) RGB image, (b) IR image, (c) depthmap before leakage compensation and (d) RGB image, (e) IR image, (f) depthmap after leakage compensation.

## Slide 40: Functional Results
Far
Near
(a)
(b)
(c)
(d)
(e)
(f)
Fig. 1.4. Results at TL84 light source (a) RGB image, (b) IR image, (c) depthmap before leakage compensation and (d) RGB image, (e) IR image, (f) depthmap after leakage compensation.

## Slide 41: Functional Results
Far
Near
(a)
(b)
(c)
(d)
(e)
(f)
Fig. 1.4. Results at U35 light source (a) RGB image, (b) IR image, (c) depthmap before leakage compensation and (d) RGB image, (e) IR image, (f) depthmap after leakage compensation.

## Slide 42: Functional Results
Depth map result at U35
RGB
IR
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 15cm
Patch size : 35x35
Search range : -16 ~ 7 pixels
Light source : U35
Far
Near
<Aperture shape>
(a)
(b)
(c)
Fig. 1.5. Results at U35 light source (a) RGB image, (b) IR image, (c) original depth map

## Slide 43: Functional Results
Depth map result at U35
RGB
IR
<Test setting>
Image size : 978x616 10bits
Color channel : Red
Focus distance : 15cm
Patch size : 35x35
Search range : -16 ~ 7 pixels
Light source : U35
Far
Near
<Aperture shape>
(a)
(b)
(c)
Fig. 1.6. Results at U35 light source (a) RGB image, (b) IR image, (c) leakage compensated depth map

## Slide 44: 2. Noise Reduction(NR)

## Slide 45: Introduction
The aim of noise reduction is to reduce the noise of raw images to improve the accuracy of edge extraction and depth estimation by
  Enhancing Signal to Noise Ration (SNR), and
  Preserving edges and textures in the image.
Far
Near
Fig. 2.1. (a) Input scene, (b) depthmap from noisy input images and (c) depthmap from temporally averaged (high PSNR) images.
(a)
(b)
(c)

## Slide 46: Functional Overview
There are numerous noise reduction methods available.
  These include
    Fixed kernel filters (Box, Gaussian)
    Guided filter (GF)
    Bilateral filter (BF) and Directional Bilateral filter (DBF)
    BM3D
  We have evaluated these methods based on PSNR and Depthmap improvement.
  BF and DBF have shown the best performance based on quantitative and qualitative depthmap evaluation.
  Considering computational complexity, BF was decided to be the suitable candidate for OA.

## Slide 47: Functional Description
Bilateral Filter
  The objective of bilateral filtering is to smoothen the image while preserving textures and edges.
  Contrary to standard fixed kernel filters (Box, GF), which only take into account the geometrical proximity of pixels, BF considers intensity similarities as well.
    Filtered output qi is calculated by
      i: current pixel location
      j: neighbor pixel location
    The parameters and control the sensitivity of the filter in domain and range respectively.

## Slide 48: Functional Results
BF
Method | Error% | MSE
Box | 42% | 10.6
GF | 46.3% | 10.3
BM3D | 48% | 15.6
BF | 36% | 8.1
Reference
Box
BF shows better performance in terms of depth classification error percentage and MSE
This comes from the fact that these filters preserve details within the image, which is important in stereo matching
Table I
Percent of bad depth and mean square error of disparity
Fig. 2.2. (a) Reference image, (b) depthmap extracted from the noisy image, (c) depthmap extracted from temporally averaged image (benchmark) and (d) depthmap extracted after applying bilateral filter to input images.
(b)
(c)
(d)
(a)

## Slide 49: 3. Integer Disparity Estimation(IDE)

## Slide 50: Introduction
Disparity evaluation is based on comparison of stereo images.
Best match for each pixel in the reference image is searched for in the target image.
To find the best match, different similarity metrics are used.
OA presents a unique challenge as the two stereo images are at a different scale and may not be correlated.
For this, a similarity metric is needed which is robust against radiometric differences.

## Slide 51: Functional Overview
Numerous similarity metrics were compared against each other.
These include
  Normalized Sum of Absolute difference (NSAD)
  Normalized Cross Correlation (NCC)
  Zero mean Normalized Cross Correlation (ZNCC)
  Census Transform (CT)
  Rank Transform (RT)
  Weighted Census Transform (WCT)
  Modified Weighted Census Transform (MWCT)
The results of these approaches with different images were distributed amongst five participants who voted NCC and ZNCC to be the best similarity metrics.

## Slide 52: Functional Description
The NCC between two patches A and B is given by
The ZNCC between two patches A and B is given by
NCC compensates for the scale difference between two patches.
ZNCC compensates for the difference of mean value between the two patches as well as the scale difference.

## Slide 53: Functional Results
Input scene
NCC result
ZNCC result
Fig. 3.1. Results of sparse depthmap generation.

## Slide 54: 4. Cost Aggregation(CA)

## Slide 55: Introduction
Cost volume aggregation is a method to refine depth using the depth of neighborhood pixels.
Cost aggregation can be broadly classified into two approaches.
Local Cost Aggregation
  These approaches consider the local neighborhood of a pixel to refine depth.
  Examples are box filter, bilateral filter, and guided filter.
Global Cost Aggregation
  These approaches consider pixels beyond the local neighborhood of an image to refine depth.
  Examples include Semi-global Matching (SGM) and Graph-cuts.

## Slide 56: Functional Overview
Cost volume is a 3D structure.
Each location of the cost volume stores the pixel-wise cost.
See accompanying figure for graphical illustration.
  Applying a box filter to each slice of
  the cost volume is equivalent to using an equal weight window for matching.
  Applying a bilateral filter to each slice
  of the cost volume is equivalent to
  using weights based on color similarity and proximity.
  Applying a guided filter to each slice o
  the cost volume is equivalent to using
  guided filter weights for aggregation.
Fig. 4.1. A depiction of the disparity volume. The disparity volume is made up of 5
slices (the disparity levels). Typically
cost volume maintains the SAD values,
however, in our case it stores the NCC
values.

## Slide 57: Functional Description
Semi-Global Matching (SGM) [1] aggregates cost over the
complete path to a pixel.
For example, the aggregated cost of pixels for a path
from left to right is given by
In our implementation we use four or eight paths.
We emphasize using four paths as these are feasible
for hardware implementation.
Fig. 4.2. Four paths feasible for
hardware implementation.
[1] Hirschmüller, Heiko. "Accurate and efficient stereo processing by semi-global matching and mutual information." Computer Vision and Pattern Recognition, 2005. CVPR 2005. IEEE Computer Society Conference on. Vol. 2. IEEE, 2005.

## Slide 58: Functional Results
Fig. 4.3. (a) Input scene, (b) result of SGM on a low PSNR image and (c) result of SGM on a high PSNR image.
(a)
(b)
(c)

## Slide 59: 5. Fractional Disparity Estimation(FDE)

## Slide 60: Functional Description
Fractional disparity extraction can be utilized to increase the depth resolution.
  Nearly universal formulation of fitting: minimize squares of differences between data and function
    Example: for fitting a second-order polynomial, minimize
    with respect to , and .
    Most general solution technique: take derivatives with regard to unknown variables, set equal to zero.
Chart: Disparity
| -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4
Correlation | 0.68 | 0.79 | 0.85 | 0.88 | 0.87 | 0.81 | 0.71 | 0.6
Estimated disparity before LSM is 0.
Estimated disparity after LSM is is 0.1666.
Example:
Fig. 3.1. Illustration of curve-fitting for increasing depth resolution.

## Slide 61: Functional Description
Fractional disparity extraction can be utilized to increase the depth resolution.
  Target :
    Samples: ,
  Interpretation: find x that comes “closest” to satisfying Ax=b
    i.e., minimize b–Ax
    i.e., minimize |b–Ax|
    Equivalently, minimize |b–Ax|2 or (b–Ax) T(b–Ax)
    Compute =(ATA)-1 AT , which is known as “pseudoinverse” of A
A
b
x